## Slide 1: I2C Master Controller

## Slide 2: Outline
Introduction
Theory
Methodology
Result
Conclusion

## Slide 3: Introduction

## Slide 4: About I2C
Inter-Integrated Circuit (I2C or I2C)
Developed in 1982 by Philips (now NXP)
A very common serial protocol
Used for short distance data communications
Synchronous master – slave protocol
Both master and slaves can send/receive data
Bidirectional, half duplex mode
Can run at different speeds
Two wires: Serial Clock (SCL) and Serial Data (SDA)

## Slide 5: About APB Interface
Advanced Peripheral Bus (APB)
Part of Advanced Microcontroller Bus Architecture (AMBA) protocol family.
Non-pipelined
Supports to low-bandwidth peripherals

## Slide 6: About LMMI Interface
Lattice Memory Mapped Interface (LMMI)
A simple memory-mapped address/data interface.
Supports both single and burst transactions with a maximum throughput of one transaction per clock cycle.
Supports optional wait states for slave interfaces.

## Slide 7: Theory

## Slide 8: Basic Topology
One master (or many) connected to one slave (or many) via two lines – SDA and SCL.
Each line connects to a voltage VCC or VDD by a single pull-up register.

## Slide 9: Frames
Master claims the bus by a “Start” condition.
Then it sends the address to the slave, followed by a “Read-Write” bit.
Slave acknowledges the bus and send back the “ACK” bit.
Master sends the data byte to the slave and receive the “ACK” bit one more time.
The communication is terminated by “Stop” condition.

## Slide 10: Start condition
Both lines are asserted.
“Start” condition occurs when a node first pulls SDA line LOW, then pulls SCL line LOW.
Prevents any other nodes taking control of the bus.
Master starts the clock signal when a bus is claimed.

## Slide 11: Sending address and R/W bit
Master sends a 7-bit address to the slave.
The address (unique and fixed) specifies the node master wants to communicate with.
The Read/Write (R/W) bit let slave knows which function is operated (0 - READ and 1 - WRITE).
The R/W bit is decoded with address to form an address byte.

## Slide 12: Timing relationship
SDA does not change value between rising or falling edge of the SCL.
SDA only transfers data when SCL is LOW to avoid “Start” or “Stop” condition.

## Slide 13: Sending data
“ACK” bit is sent by the slave, 0 is acknowledged and 1 is negative ack (NACK).
ACK bit is used to confirm the readiness of address or data.
8-bit data byte contains the transferred information (memory, addresses or register contents).

## Slide 14: Stop condition
Indicating the end of communication.
First SCL is asserted and remains HIGH, then SDA also do the same.
The bus will become idle, there is no clock signal and now any node can use “Start” condition to claim the bus.

## Slide 15: Sending multiple data bytes
Additional data bytes with ACK bit concatenate onto previous byte.
The data bytes can be all data or different types of variables.

## Slide 16: Methodology

## Slide 17: 1. I2C Master Controller
Block Diagram
Final State Machine

## Slide 18: 2. APB Interface
Block Diagram
Final State Machine

## Slide 19: 3. LMMI Interface
Block Diagram
Final State Machine

## Slide 20: Results

## Slide 21
I2C Master Controller - WRITE Transaction

## Slide 22
I2C Master Controller - READ Transaction

## Slide 23
APB Interface - WRITE and READ with no wait states

## Slide 24
APB Interface - WRITE and READ with no wait states (failing)

## Slide 25
APB Interface - WRITE and READ with wait states

## Slide 26
APB Interface - WRITE and READ with wait states (failing)

## Slide 27
LMMI Interface – Single WRITE with no wait states

## Slide 28
LMMI Interface – Single WRITE with wait states

## Slide 29
LMMI Interface – Burst WRITE with no wait states

## Slide 30
LMMI Interface – Burst WRITE with wait states

## Slide 31
LMMI Interface – Single READ with no wait states

## Slide 32
LMMI Interface – Single READ with wait states

## Slide 33
LMMI Interface – Burst READ with no wait states

## Slide 34
LMMI Interface – Burst READ with wait states

## Slide 35
LMMI Interface – Back-to-Back READ and WRITE with no wait states

## Slide 36
LMMI Interface – Back-to-Back READ and WRITE with wait states

## Slide 37
LMMI Interface – Back-to-Back WRITE and READ with no wait states

## Slide 38
LMMI Interface – Back-to-Back WRITE and READ with wait states

## Slide 39: Conclusion

## Slide 40: Success and Shortcoming
SUCCESS | SHORTCOMING
Design protocol of I2C Master Controller and two interfaces (APB, LMMI). Write testbench and verify all testcases for each module. | Write top module connect three modules. Maximize the flexibility of inputs to control the outputs independently.

## Slide 41: Thank you